UDC 621.397.771.537 (043.2)

V. N. Belinsky, Ph.D. lecturer

(National Aviation University, Ukraine)

INFLUENCE SIGNAL/ NOISE IN SEMICONDUCTOR MATRIXES RESOLUTION OF THE DIGITAL REMOTE SENSING SYSTEMS THE EARTH'S  SURFACE

We study the method  of determining  resolution digital remote sensing the Earth's surface to assess the quality digital images

Introduction. Statement of the problem.  In [1,2] it was proved that the resolution R of aerophotographic systems (APhS) can be defined as the point of intersection between the through contrast transfer function  of the aerial camera Ws (ν) and the curve of the film threshold contrast Kc (ν), which is determined by the threshold contrast of a decoder and the filmnoise. The practical implementation of this method has found its development when operating aerial reconnaissance, mapping aerial photography, and aerial surveillance of the Treaty on Open Skies [3]. The resolution of the aviation opto-electronic systems of air surveillance is defined similarly as for the APS (Fig. 1) [4].

Fig.1.  Contrast transfer function of the threshold contrast curve

Analytical interpretation of Fig. 1 has the form shown below :

(1)

where Dsh and Gsh-variance and power spectral noise; Sser - average signal.

Due to the advent of digital aerial cameras in which the optical image areas are recorded by the semiconductor photomatix, there is a need for scientific justification in applying this method to determine the resolution of digital aerial cameras.

The basic material research,. Semiconductor sensors of video signal are currently being built on the basis of the silicon photodiods matrix or charge-coupled device (CCD). The best parameters and characteristics are possessed by conditioners based on video files - SIP, which turn the light signal (optical image)  into electrical signal charges (video). The principle of photo-SIP is based on the properties of the registry, consisting of MOS capacitors that are near located in the line. The transfer of charge packets, the size of which is proportional to the magnitude of exposure is controlled by signal charge transfer by clock pulses [1].

The MOS capacitor (Fig. 1) serves as the basis of photo-CCD.

electrode

potential

pit

silicon oxide

p-silicon

+U

Fig. 2. MOS - capacitor.

electrode

potential

pit

silicon oxide

p-silicon

+U

Fig. 2. MOS - capacitor.

The semiсonducting silicon substrate, for example p-type, is covered with a layer of silicon oxide dielectric, the thickness of which is  microns, above which the partially transparent metal electrode (gate) is located. Semiconductor substrate and a metal electrode acts as a cover for  MOS - capacitor, the specific capacity of which is equal to [4]:

,                                           (2)

where - relative dielectric constant insulator (silicon oxide). If the shutter apply the benefits of the conservation of charge  (voltage storage), the minority carriers (electrons) will gather directly under the electrode near the surface of the semiconductor and the major carriers (holes) will move into the interior volume of the semiconductor, because they will be repelled from the electrode. Thus, a free mobile hole depleted region depth  will appear  under the electrode on the boundary oxide - semiconductor. In this region, called a pit potential, the charge density is:

,

where   - the concentration of acceptor; - the electron charge. The distribution of potential within the depleted region along the axis Ox can be obtained by the decision of Poisson equation:

,                                                          (3)

where  - relative dielectric constant of silicon (semiconductor).

Integrating, equation (3) with boundary conditions at, , ,    (2) we obtain the potential distribution in the form:

,

where - the so-called deep potential well.

The potential on the boundary of separation  is called the surface potential:

.                                                         (4)

When the equilibrium conditions according to Kirchhoff law can be written, the potential charge saving package:

(5)

where  and  - the voltage drop in silicon and its oxide, respectively.

Given that

and                                                      (6)

,                                         (7)

where  - the potential of a plane curve of the bottom of the valence band. Сombining (4) - (7), we obtain:

,                     (8)

When completely filled potential well  , and the conductivity of the surface inverted, that is two the potential of the Fermi level:

(9)

Substituting (8) in (7) and given the fact that in practice the left hand side of (7) is always much more right, the expression for the maximum surface density of carriers in filled potential well will look like:

,                                                 (10)

.                                                       (11)

For a typical size of the square potential well bottom ( microns)  possible maximum number of electrons in the pit will be:

.                                                (12)

If the minimum possible    and    the depth of potential   well is located within a few micrometers.

Suppose that a MOS - capacitor from the gate drops optical radiation with a wavelength , creating energy light    . Then the radiation flux absorbed by the potential pit is equal   . This flow corresponds to the number of photons absorbed per  second

,                                               (13)

where h = 6,62 * Planck's constant; c-speed of light in the semiconductor, m / s. Multiplying (12) during the accumulation of charges (exposure time ) and quantum efficiency, we obtain the number of electrons accumulated in the potential dep well (charuntsi):

.                                            (14)

Calculations show that the conditions for the earth's surface of signal electrons in charuntsi 2-3 is hundreds of thousands.

If this minimum number of electrons is limited to the influence of noise  (), then dividing  by  , we get the dynamic range of  MOS - capacitor.

The minimum signal package that can be gained charuntsi determined noise level [3].

CCD noise at low light levels measured value of noise equ ivalent signal induced threshold number of photons, which provides the output of signal / noise ratio - S / N = 1.

Noise CCD can be determined analytically, given the noise of the following sources: noise Naykvysta address key and reset key of dispersion noise charge  - where   - capacity potential well for noise at the output key, and   - the absolute temperature MOS - capacitor, noise and on the surface  intensive traps in the sensitive element and the shift register having a variance , where C - effective capacity traps, shot noise detector and register shift is due to dark current -, where tн  - time savings, and  - current termoheneratsiyi and e - electron charge; noise resulting from the inefficiency of the transfer , with dispersion  .

In this way noise charge packet

,                          (15)

where  - the number of transfers charge packets. NEP not be less noise Naykvysta key reset, the average noise charge is equal to 200 electrons in the original containers . To significantly reduce noise reset using a special method of signal processing method called double  korrelovanoyi sample the essence of which is that of output voltage noise is subtracted . As a result, there is separation of noise from the reset signal charge and simultaneously eliminated the noise type

Thus, one can say that the noise level (rms) in current photo-CCDs, operating at frequencies ΔB = 5-10 MHz (= 1/25-1/30 s), is dozens of electrons. And the noise variance - a few hundred electrons. That is, the value of the minimum video signal ("black” level) Nbl =10 - 30 electrons, and the amplitude of the spatial harmonics - Ns = (Nwh-Nbl) / 2, and the level of middle-Nm = (Nwh + Nbl) / 2.

The inertia of the CCD is determined by the transit time of carriers under the gate, c: a person

,                                                              (16)

where b - size of the electrode along the direction of charge transfer package, m; μ - mobility of minority carriers; E - the accelerating electric field, V / m Then the bandwidth is, Hz:

.                                                                  (17)

Velocity of a charge coupled package is equal to, м/s:

,                                                                    (18)

where Δν = 1/2b - spatial bandwidth in the ССD matrix plane, мм-1 .

Conclusion

Thus, substituting the value  та  to (1), one can determine the resolution of any digital aerial camera.

References

1. Jones R.C., J. Opt. Soc. Am., 50, 883 (1960)

2. Х.Фризер. Фотографическая регистрация информации. – М.:Мир, 1978. - 427с.

3. T.Orhaug ,  C.Hugo Agren.  F0A  Report C , 30666-9.4. September,  1992. - С.22.

4. Белинский В.Н. Поздеев С.Т. Авиационная оптико-электроника и светотехника. - К.: КВВАИУ, 1988. - 319 с.

5. Хромов Л.И., Лебедев Н.В., Цыцулин А.К., Куликов А.Н. Твёрдотельное телевидение. - М.: Радио и связь, 1986. -185с.

6. Цифровое преобразование изображений: Уч. пособие для вузов/Быков Р.Е., Фраер Р., Иванов К.В., Манцветов А.А; под ред. проф. Р.Е. Быкова.-М.: Горячая линия - Телеком, 2003. - 228 с.

7. Бєлінський В.М. Вплив характеристик напівпровідникових датчиків відеосигналу на якість телевізійного зображення. Зб. Матеріали Міжнародної науково-практичної конференції „Україна в Євроінтеграційних процесах”. – К.: КиМУ. 2007. – С. 26-31.